## Slide 1: Traffic Light Controller – RTL Design
FSM-Based Verilog Implementation

## Slide 2: Overview
• FSM-based control of a traffic light sequence
• State transitions: IDLE → RED → YELLOW → GREEN → IDLE
• Each state enables a specific light for a duration
• Designed using Verilog with a basic testbench

## Slide 3: FSM State Transition
• IDLE: All lights OFF
• RED: Red ON (50ns)
• YELLOW: Yellow ON (30ns)
• GREEN: Green ON (70ns)
• Transitions triggered by clock and 'start' input

## Slide 4: RTL Verilog Implementation
• Two always blocks:
– PSR (Present State Register): Sequential logic with async reset
– NSOL (Next State & Output Logic): Combinational logic
• Case-based state transition and output generation
• Uses 2-bit state encoding for 4 states

## Slide 5: Testbench Structure
• DUT instantiation and input stimulus
• Clock generation and reset handling
• 'start' toggled to initiate state transition
• Outputs monitored via waveform (ModelSim/GTKWave)